## Slide 1
TRANSPORTATION — INNOVATED.
SpaceX Hyperloop Technical Presentation University of Waterloo Hyperloop Team
University of Waterloo—Hyperloop Final Design Package | 1

## Slide 2
University of Waterloo—Hyperloop Final Design Package | 2
HYPERLOOP VIDEO

## Slide 3
University of Waterloo—Hyperloop Final Design Package | 3
TEAM INTRODUCTION
Technical Design
Drive Train
Exterior Design
Levitation
Pod Body Design
Embedded System
Braking
Thermal Analysis
Interior & Vibration
Battery
Industrial Design
Safety
Management

## Slide 4
University of Waterloo—Hyperloop Final Design Package | 4
"A designer knows he has achieved perfection not when there is nothing left to add, but when there is nothing left to take away.“
--- Antoine de Saint Exupery

## Slide 5
University of Waterloo—Hyperloop Final Design Package | 5
DESIGN PHILOSOPHY
Functional
Achievable
Simple
Testable

## Slide 6
University of Waterloo—Hyperloop Final Design Package | 6
GENERAL POD SUMMARY (GONE?)
Weight (total only)
Power requirement
Max speed
Dimensions
Method of levitation/propulsion

## Slide 7
University of Waterloo—Hyperloop Final Design Package | 7
700 kg
Approximately 1500lbs total weight

## Slide 8
University of Waterloo—Hyperloop Final Design Package | 8
1.5 kW
Required power, mainly for controllers
~2 hp

## Slide 9
University of Waterloo—Hyperloop Final Design Package | 9
335 km/hr
Top Speed
equivalent to 208mph (93m/s)

## Slide 10
University of Waterloo—Hyperloop Final Design Package | 10
$48,000
Estimated Construction Cost including 30% contingency

## Slide 11
University of Waterloo—Hyperloop Final Design Package | 11
POD DIMENSIONS
1320 mm wide (52”)
850 mm high (34”)
3100 mm long (122”)

## Slide 12
University of Waterloo—Hyperloop Final Design Package | 12
LEVITATION

## Slide 13
University of Waterloo—Hyperloop Final Design Package | 13
AIR STORAGE

## Slide 14
University of Waterloo—Hyperloop Final Design Package | 14
LATERAL CONTROL

## Slide 15
University of Waterloo—Hyperloop Final Design Package | 15
POD BODY
Al-505
  12 ga. = 2mm
Low Cost
No pressure boundary

## Slide 16
University of Waterloo—Hyperloop Final Design Package | 16
INTERNAL FRAME
Al 6061
  HSS 2”x2”x⅛”
Ease of manufacture

## Slide 17
University of Waterloo—Hyperloop Final Design Package | 17
POD BODY - AERODYNAMICS
CD = 1.42
Kantrowitz limit
  max area 1.92 m2 > 0.77 m2
FD = FSkin + FPressure = 1.9 + 8.5 = 10.4 N

## Slide 18
University of Waterloo—Hyperloop Final Design Package | 18
BRAKING: EDDY CURRENT
100 m/s to 60 m/s = 46% KE remaining

## Slide 19
University of Waterloo—Hyperloop Final Design Package | 19
BRAKING: EDDY CURRENT
48 neodymium permanent magnets
Energy fully removed
Fail safe

## Slide 20
University of Waterloo—Hyperloop Final Design Package | 20
BRAKING: FRICTION

## Slide 21
University of Waterloo—Hyperloop Final Design Package | 21
BRAKING: FRICTION

## Slide 22
University of Waterloo—Hyperloop Final Design Package | 22
DRIVE TRAIN – IDLER WHEELS
Usage Scenario
Recovery Mode( Protect Air Casters )
Drive Mode ( Lower power needed to maintain motion )
Design
High Speed ( 10,000 RPM )
High Load ( 400 lbs ea. )
Vibration Dampening( Up to 26Hz )

## Slide 23
University of Waterloo—Hyperloop Final Design Package | 23
DRIVE TRAIN – POWER TRANSMISSION
Recovery Mode
Drive Mode
Motor Specifications
Max Speed | 2 m/s
Acceleration | 0.1 m/s^2
Wheel Radius | 0.1m
Torque | 7.62Nm
Power | 150W

## Slide 24
University of Waterloo—Hyperloop Final Design Package | 24
DRIVE TRAIN – CLUTCH
Clutch Design
Method of Actuation | 2 m/s
 | 0.1 m/s^2
Wheel Radius | 0.1m
Torque | 7.62Nm
Power | 150W

## Slide 25
University of Waterloo—Hyperloop Final Design Package | 25
BATTERY - OUTLINE
Specs
4 x 24V Cells for Drive Motor
1 x 24V Cell for Clutch Actuator
15Ah per Cell (2C)
30A Max Current Draw
Energy density > power density for long servicing time
Testing Plans
Cycle testing
Overloading
Extreme Environment
Vibrations

## Slide 26
University of Waterloo—Hyperloop Final Design Package | 26
BATTERY - OUTLINE
Specs
4 x 24V Cells for Drive Motor
1 x 24V Cell for Clutch Actuator
15Ah per Cell (2C)
30A Max Current Draw
Energy density > power density for long servicing time
Testing Plans
Cycle testing
Overloading
Extreme Environments
Vibrations
Battery Cells
Inner Shell
Cooling Coil
Vibration
Dampening
Outer Shell
Show some THERMAL stuff from jake here

## Slide 27
University of Waterloo—Hyperloop Final Design Package | 27
COMMUNICATION
Communication Notes
Using SpaceX recommended communication line
What will we communicate?
Camera feeds
polling sensor data
pinging to check communication line integrity
emergency stop
race start initiation

## Slide 28
University of Waterloo—Hyperloop Final Design Package | 28
EMBEDDED SYSTEM/COMMUNICATION
Primary and Secondary Controller Board
Arcturus uC5328
uCLinux OS
Large support community
Self Monitoring
Each board monitors the other
Primary down → Secondary controlled stop
Arcturus uC5328

## Slide 29
University of Waterloo—Hyperloop Final Design Package | 29
SENSORS
Sensor Considerations
Operating temperature range
Noise from physical vibrations
Sensor response time

## Slide 30
University of Waterloo—Hyperloop Final Design Package | 30
SAFETY
Usman
Thermal Isolation
Vibration Dampening
Vacuum Protection

## Slide 31
University of Waterloo—Hyperloop Final Design Package | 31
FMEA
Part | Failure Mode | Potential Cause | Probability (Estimate) | Severity | Detection | Risk Level
Frame | Catastrophic Failure | Excessive pusher load or severe impact | C | V | 5 | High
Brake Pads | Loss of braking ability | Cooling system malfunction resulting in brake pad degradation | A | V | 5 | High
Batteries | Explosion/fire | Overcharging | C | V | 5 | High
Air Casters | Friction underneath casters | Overloading air casters | B | I | 2 | Moderate
Brake Pad Mounting | Structural Failure | Excessive forces surpassing safety tolerances | A | V | 5 | Moderate

## Slide 32
University of Waterloo—Hyperloop Final Design Package | 32
SAFETY MECHANISM FOR POWER LOSS
Battery System
  Backup spare battery will take over system electronics immediately.
Levitation System
  Main air supply will shut-off. Air casters will deflate to allow the pod to rest on idler wheels and prevent air caster damage.
Braking System
  Vent valves will fail-open to actuate the brake system upon power loss or control signal loss

## Slide 33
University of Waterloo—Hyperloop Final Design Package | 33
FAULT TOLERANCE OF CRITICAL SYSTEMS
Braking
2 sets of friction brakes (4 pads) to overcome mechanical failure
Eddy current brakes engaged simultaneously through integrated actuation
Primary and secondary controllers maintain brake system control at all times
Controls
Primary System – Main pod systems control
Secondary System – Monitoring and emergency protocol, maintains active signal for controlled braking
Primary Control System
Secondary Control System
Levitation Systems
Drivetrain System
Battery Systems
Braking System (Failsafe)
Sensors and Actuators
Activate Emergency Protocols
System Failure

## Slide 34
University of Waterloo—Hyperloop Final Design Package | 34
FAULT TOLERANCE OF CRITICAL SYSTEMS
Drivetrain
Mechanism itself is a fault tolerant procedure in case power, control, cooling or levitation system failure
Levitation
Pod weight shifts on to idler wheels in case of levitation system failure
Idler wheel
Air Caster
CAM Raised
Wheel Raised (gap)
Wheel in Contact (no gap)
CAM Lowered

## Slide 35
University of Waterloo—Hyperloop Final Design Package | 35
SUBJECT FOR RE-DESIGN
method of lateral control
pod length
subtle shell mounting and contour shape
mounting of idler wheels
location of the pusher interface

## Slide 36
University of Waterloo—Hyperloop Final Design Package | 36
SCALABILITY

## Slide 37
University of Waterloo—Hyperloop Final Design Package | 37
FULLSIZE SPECIFICATIONS
Capacity: 26 passengers per pod
Interior diameter: 2 meters
Top speed: ~1220 km/h
Cost: ~ $500,000 per pod

## Slide 38
University of Waterloo—Hyperloop Final Design Package | 38
FULLSIZE SPECIFICATIONS
Modular Component
  Easier to scale and maintain
Kantrowitz limit
  Need to be considered
Linear induction motors
  Will be used for operational acceleration and deceleration
Passenger ergonomics considerations
  HVAC, entertainment, interior design etc

## Slide 39
University of Waterloo—Hyperloop Final Design Package | 39
SPONSORSHIPS
Kik - Major sponsor
University of Waterloo (WEEF, Eng Soc)
Solidworks
Babylon VR

## Slide 40
University of Waterloo—Hyperloop Final Design Package | 40
ADDITIONAL DOCUMENTS & SLIDES